## Slide 1
Available Data

## Slide 2
Hcana reconstructed cluster quantities  NPS.Cal.*
Reconstructed kinematics  NPS.kin.Secondary.*
Cluster info taken from vtp trigger  NPS.Cal.vtp*
RUN 4454, Seg 0
Cluster size
# of clusters
Cluster time

## Slide 3
Cluster XY pattern from hcana and vtp
calibrated
vtp
Assume vtp data is all we see,
Ever moved the nps during the experiment ?
ML model do not know the calibration and treat the XY hit the same way

## Slide 4
Timing info from Josh
Cuts
  Hms triggered
  Cluster E > 0.6 GeV
  Cluster time within some window
For each pixel:
  NPS.cal.fly.block_clusterID (number in the plot) NPS.cal.fly.goodAdcTdcDiffTime (color)

## Slide 5
Waveform data from replay
Flatten vector of waveforms
Only active blocks are stored
Length of waveform = 110 (each 4ns)
1 waveform can have multiple pulses/hits
2 element used to store block id and length
Total length = nblocks * (110 + 2)

## Slide 6
Waveform data from replay

## Slide 7
VTP
  Use 3x3 grid to determine trigger
  center position of vtp cluster
  (color represent total energy within the grid)

## Slide 8
Blocks with waveform and cluster found by hcana

## Slide 9
Frame construction

## Slide 10
How to pack data to a frame
A time gap between events determined by the TI module which measures the start time of the events
  Branch : g.evtime
  If coda version > 3, TI time is already decoded in THaEvData,
  Else it is set from THcHelicityReader ?
Estimated as pedestals in the previous event
waveforms
Gap between 2 events
waveforms
440ns
? ns
2
Structure of a frame in SRO
110 time buckets = 440ns

## Slide 11
How to pack data to a frame
A time gap between events determined by the TI module which measures the start time of the events
  Branch : g.evtime (unit = ns ???)
  Large gap so one frame is just one event + some pedestal ?
waveforms
Gap between 2 events
waveforms
440ns
? ns
2
110 time buckets = 440ns

## Slide 12
Model

## Slide 13
Graphical Neural Network (No result yet)
Each event = 1 graph
Each active block = 1 node
Edges are drawn between 2 nodes if the distance is smaller than where r is the unit length of a block
Edges weights are scaled accordingly
Node attribute = waveform (with pedestal if use frame instead of 1 event)

## Slide 14
Model
smaller goal
  ignore true timing, energy
  only classify the members of each clusters
Input tensors
(imagine no edge here)
Nx
Edge construction in latent space
Pos embedding to keep the temporal info
Garnet/Gravnet
Takes the neighbour and compute new features
Another kNN edges
Should be modified later
Compare with truth edges  bce loss

## Slide 15
Message Passing
Graph operation which only takes the features from connected nodes
Generalize convolution
Permutation invariant function (sum , mean)
Since we are dealing with a time series, replace it with lstm, attention ?